## Slide 1: Università degli Studi di Modena e Reggio Emilia UNIMORE
Research Grant:
Main Topics
Dipartimento di Ingegneria "Enzo Ferrari"
Research grant holder: Pietro Braglia

## Slide 2: Brief presentation
Bachelor’s degree:
  “ Progettazione di controllo PID”, UNIMORE
Master’s degree:
  “Modeling and control of a Multi Mode Hybrid Architecture with e-CVT & PTO”, UNIMORE
Job experience
Research grant holder

## Slide 3: Rsearch grant topics
Hairpin technology (from 11/2019 to 01/2020)
Inverter structures for active voltage overshoot filtering (from 01/2020 to 10/2020)
Design of more-electric tractors for a more sustainable agriculture (PhD main topic)

## Slide 4: Main topics
Round vs Rectangular conductors: Hairpin choice
  Round conductor
  Rectangular shape: Hairpin
Manufactory process of Hairpin
Proposal architectures for motor design with hairpin
  Segmented Hairpins

## Slide 5: Power icrement contributes
Torque | Speed
Air gap flux density E.g. improved electromagnetic properties of materials Linear current density E.g. new cooling systems and improved thermal management Operating conditions E.g. innovative tools of analysis, optimal control | Mechanical properties of materials E.g. increased yield strength with no impact on magnetic properties Optimal machine design E.g. optimal pole pair Number Parasitic effects E.g. compensation for skin effect, increased reliability
Winding technologies | 
Decrease winding resistance (larger wire diameters, reduced end winding lengths) Decrease AC parasitic effects (multi-stranded and optimal end winding shape) Increase fill factor | 

## Slide 6: Round conductors
Basic winding pattern:
Stator design solution for winding positioning:
segmented stator
laminated plug-in tooth

## Slide 7: Rectangular conductors
Round conductors left some empty space in the slot due to geometrical shapes…
Basic idea: fullfill rectangular slot with rectangular conductors
Solution:
Hairpin

## Slide 8: Manufactory main phases
Preparatory phase: straightening, stripping and cutting
Manufactory process: Shaping of the rectangular conductors, assembly in the stator, mechanical twisting, contacting
Contacting phase changes for mass production and prototyping
Shaping | Assembly | Twisting | Contacting

## Slide 9: Contacting techniques
Mass production requires low cycle time, high reliability, automation of the process: Laser welding
Prototyping phase accepts high cycle time saving costs: soldering

## Slide 10: Innovative geometry: segmented hairpins
Basic idea:
Design of parallel paths in the slots
Benefit:
Further reduction of current density peaks with respect to asymmetric solution
Drawback:
Complex manufactory

## Slide 11: ISIE 2020 3 June 2020
Challenges and Future Opportunities of Hairpin Technologies

## Slide 12: Reference architectures
Inverter 2-levels
Inverter 3-levels
Inverter 3-levels T-type
Inverter 2-levels T-type β-delay
Multi-Leg (Kolar type)
Proposed Solution

## Slide 13: Inverter 2-levels – basic case
Single carrier wave, three modulating waves
SiC MOS must be able to sustain 1200 V
High THD due to 2 levels limitation
Reference transistor model C3M0075120K

## Slide 14: Inverter 3-levels
Two carrier wave, three modulating waves
SiC MOS must be able to sustain 600 V
Lower THD with respect to 2 levels inverter
Two clamping diodes for each inverter’s leg
Doubled number of transistor with respect to 2 levels inveter
Reference transistor model SCT3080AR

## Slide 15: Inverter 3-levels T-type
Two carrier wave, three modulating waves (POD PWM)
For each leg: 2 devices must be able to sustain 1200 V, the other 2 (mid-point) 600V
Lower THD with respect to 2 levels inverter
Doubled number of transistor with respect to 2 levels inveter
Lower conduction losses compared to conventional 3 level
reduction of THD depending on the chosen PWM technique

## Slide 16: Inverter T-type β-delay
Insertion of step at every transition of PWM voltage for where depends on line characteristics, i.e.
Reduction of voltage overshoot based on reflection of the wave
Doubled number of transistor with respect to 2 levels inverter
Minimum additional losses (two additional devices are conducting just for time )

## Slide 17: Multi-leg converter – 2 levels
Reduction of obtained placing more legs in parallel, the result with parallel legs cause a voltage gap in time equivalent to
Reduction of voltage overshoot
Controlled equalized distribution of high load currents to individual bridge-legs can be achieved
Every 2 legs, 1 coupling inductors is required (M2 and M3) with , every 2 transformers will be connected to another coupling one (M4)
More devices but with lower current Pcond=RI^2
In the example:
It is expected to observe

## Slide 18: Multi-leg converter – 4 levels (Kolar)
Blue line contains the 2 level architecture
Increasing , the number of transistors will be per phase
will be reduced
In the example:
A single phase circuit contains 4 legs, 3 coupled inductor, a modulating wave.

## Slide 19: 4 levels case – Voltage Phase to GND (detail)
Carrier frequency 10.000 Hz
Modulating frequency 50 Hz
,

## Slide 20: Proposed solution
Blue line contains Beta inherit solution
Red line contains Multi-Leg (Kolar) inherit solution

## Slide 21: Simulation results
In the following slides, simulations results of the previous architectures are compared:
control is imposed to obtain 5 A, 10 A, 20 A peak current on the load.
Three different values of are imposed 500 V, 600 V and 800 V
Three different values of carrier frequency for PWM are imposed: 10k Hz, 20k Hz, 40k Hz
N.B: a resistance of 2mΩ is placed in series to each winding in the coupled inductors present in Multi-Leg (Kolar) architecture and in the proposed one

## Slide 22: Simulation results – 800 V 10kHz
Switching losses: blue
Conduction losses: green

## Slide 23: Simulation results – 800 V 20kHz
Switching losses: blue
Conduction losses: green

## Slide 24: Simulation results – 800 V 40kHz
Switching losses: blue
Conduction losses: green

## Slide 25: Reliability calculations
2 level invereter & Beta 2 level inverter
For both 2 level inverter and Beta inverter, the phase reliability function is dependent only from 1 single device.
For reliability study, the following assumptions are taken:
Main failure mechanism is bond wire lift-off
number of cycles, depends thermal cycle

## Slide 26: Reliability calculations
Kolar
For Kolar inverter, after the transient, n SiC MOS work in parallel, here n=4, so the reliability is defined by the formula defined above.
3 level inverter
For 3 level inverter, the series of 2 SiC MOS is always maintained per phase so the reliability of the phase is equivalent to the product of the elements in series.

## Slide 27: Reliability calculations
Proposed solution
For Proposed solution inverter, the 2 MOS in series guarantee the 0 V level, n SiC MOS work in parallel, here n=2, so the reliability is defined by the formula defined above.
T-type
In T-type inverter, considering M=0.5, half of the period the output is at 0V and the other half at V_dc. During the former, 2 SiC MOS are in series per phase and during the latter a single SiC MOS is working.

## Slide 28: Reliability summary
2 level & Beta | 3 level | Ttype | Kolar | PS
2 level & Beta | 3 level | Ttype | Kolar | PS
Note: t expressed in cycles

## Slide 29: Bibliography
"Reducing dv/dt of Motor Inverters by Staggered-Edge Switching of Multiple Parallel SiC Half-Bridge Cells“, T. Fuchslueger, TU Wien/Power Electronics Section, Austria, thomas.fuchslueger@tuwien.ac.at M. Vogelsberger, Bombardier Transportation Austria GmbH, PPC/GSC-Drives, Austria H. Ertl, TU Wien/Power Electronics Section, Austria
"An Overvoltage Suppression Scheme for AC Motor Drives Using a Half DC-Link Voltage level at Each PWM Transition", Sangcheol Lee, Student Member, IEEE, and Kwanghee Nam, Member, IEEE
"The Operation of Auxiliary Resonant Commutated Pole (ARCP) and Its benefits for Electric Motor Drives" , James Hamond, Derek Kroes, Bruce Renouard, Nigel Springett
"Design and Implementation of 3-Phase 3-Level T-type Inverter with Different PWM Techniques", Amit Singh Jadon Department of Electrical Engineering Madhav Institute of Technology & Science Gwalior, India, Praveen Bansal Department of Electrical Engineering Madhav Institute of Technology & Science Gwalior, India, Dr. Anmol Ratna Saxena Department of Electrical & Electronics Engineering National Institute of Technology Delhi, India
"Advanced 3-ΦSiC/GaNPWM Inverter & Rectifier Systems", J.W. Kolar, M. Guacci, M. Antivachis, D. Bortis, Swiss Federal Institute of Technology (ETH) Zurich, Power Electronic Systems Laboratory, www.pes.ee.ethz.ch
"Time-Dependent Dielectric Breakdown of 4H-SiC MOS Capacitors and DMOSFETs", K. Matocha, G. Dunne, S. Soloviev and R. Beaupre, in IEEE Transactions on Electron Devices, vol. 55, no. 8, pp. 1830-1834, Aug. 2008, doi: 10.1109/TED.2008.926595.
Yu, Liangchun & Dunne, Greg & Matocha, Kevin & Cheung, Kin & Suehle, John & Sheng, Kuang. (2011). Reliability Issues of SiC MOSFETs: A Technology for High-Temperature Environments. Device and Materials Reliability, IEEE Transactions on. 10. 418 - 426. 10.1109/TDMR.2010.2077295.

## Slide 30
Thank you for your attention