## Slide 1: ISIE 2020 3 June 2020
Challenges and Future Opportunities of Hairpin Technologies
Pietro Braglia, Stefano Nuzzo, Davide Barater

## Slide 2: Main topics
Electric vehicle power discussion
  Power requirements
  Power increment contributes
Round vs Rectangular conductors: Hairpin choice
  Round conductor
  Rectangular shape: Hairpin
Manufactory process of Hairpin
  Manufactory main phases
  Contacting techniques
  Reference standard for sizing
Proposal architectures for motor design with hairpin
  Standard Hairpin winding
  Asymmetric Hairpins
  Segmented Hairpins
  Thermal comparison

## Slide 3: Power requirements
Electrification of vehicle is taking relevant role in automotive, marine and aerospace.
Maximisation of power-to-weight and torque-to-weight ratios represents the primary objective.
Power requirements are increasing so the main aspects for design:
  Torque
  Speed
  Winding technologies

## Slide 4: Power icrement contributes
Torque | Speed
Air gap flux density E.g. improved electromagnetic properties of materials Linear current density E.g. new cooling systems and improved thermal management Operating conditions E.g. innovative tools of analysis, optimal control | Mechanical properties of materials E.g. increased yield strength with no impact on magnetic properties Optimal machine design E.g. optimal pole pair Number Parasitic effects E.g. compensation for skin effect, increased reliability
Winding technologies | 
Decrease winding resistance (larger wire diameters, reduced end winding lengths) Decrease AC parasitic effects (multi-stranded and optimal end winding shape) Increase fill factor | 

## Slide 5: Round conductors
Basic winding pattern:
Stator design solution for winding positioning:
segmented stator
laminated plug-in tooth

## Slide 6: Rectangular conductors
Round conductors left some empty space in the slot due to geometrical shapes…
Basic idea: fullfill rectangular slot with rectangular conductors
Solution:
Hairpin

## Slide 7: Manufactory main phases
Preparatory phase: straightening, stripping and cutting
Manufactory process: Shaping of the rectangular conductors, assembly in the stator, mechanical twisting, contacting
Contacting phase changes for mass production and prototyping
Shaping | Assembly | Twisting | Contacting

## Slide 8: Contacting techniques
Mass production requires low cycle time, high reliability, automation of the process: Laser welding
Prototyping phase accepts high cycle time saving costs: soldering

## Slide 9: Reference standard for sizing
Sizing in rectangular conductors is predisposed by IEC60317-0-2 standard defining the recommended thickness vs width depending on the insulator grade

## Slide 10: Standard hairpin winding
Conventional hairpin windings:
conductor size is fixed
current density is not omogenously disposed in the slot
Higher losses near the slot opening

## Slide 11: Innovative geometry: asymmetric hairpins
Basic idea:
Size reduction of conductors near the slot opening
Benefit:
Current density peaks reduction
Drawback:
It requires conductors of different size

## Slide 12: Innovative geometry: segmented hairpins
Basic idea:
Design of parallel paths in the slots
Benefit:
Further reduction of current density peaks with respect to asymmetric solution
Drawback:
Complex manufactory

## Slide 13: Thermal comparison
Loss reduction also affects the operative temperatures of the motor with non-negligible improvements
TMAX=169°C
TMAX=145°C
TMAX=139°C

## Slide 14: Thank you for your attention